## Slide 1: Gazebo Plugin - Bumper -

## Slide 2
Gazebo Bumper Plugin
<Gazebo Plugin Documentation>
http://gazebosim.org/tutorials?tut=ros_gzplugins

## Slide 3
<gazebo reference="{Robot_link_name}"> # ex) turtlebot3_body_link
<sensor type="contact" name="{Robot_contact_sensor_name}"> # ex) turtlebot3_contact_sensor
<update_rate>10.0</update_rate> # hz, Topic Transmission rate(speed)
<always_on>true</always_on>
<contact>
<collision>{Collision_name}</collision> # 이 부분은 뒷 장에 SDF파일에서 얻을 수 있음.
</contact>
<plugin name="{Plugin_name}" filename="libgazebo_ros_bumper.so"> # ex) turtlebot3_body_link_plugin
<bumperTopicName>{ROS_Topic_name}</bumperTopicName> # ex) turtlebot3/gazebo_contact
<frameName>{Robot_link_name}</frameName> # ex) turtlebot3_body_link
</plugin>
</sensor>
<mu1>0.2</mu1>
<mu2>0.2</mu2>
<selfCollide>true</selfCollide>
<material>Gazebo/white</material>
</gazebo>
Your_Robot_gazebo.xacro File
'ex)': {}안에 들어갈 예시

## Slide 4
SDF File
$ cd {Your_ROS_Catkin_workspace/urdf directory}
$ rosrun xacro xacro --inorder contact_robot.xacro > contact_robot.urdf
$ gz sdf -p contact_robot.urdf > contact_robot.sdf
SDF file에서 {Robot_link_name}에 해당하는 부분의 <link>를 찾고, <Collsion>의 name을 복사해서 gazebo.xacro file의 contact sensor <contact>에 붙여넣는다.
만약 urdf.xacro file의 <collision> 부분에 naming을 하고 싶으면,
urdf.xacro file에서 <collision name="{Collision_name}">으로 만들고,
위와 같이 sdf파일 생성 후 sdf파일의 Collision name을 복사 붙여넣기를 해도 된다.
참고자료:
https://answers.ros.org/question/246448/getting-contact-sensorbumper-gazebo-plugin-to-work/

## Slide 5
Callback function(python)
# import gazebo msgs
from gazebo_msgs.msg import ContactsState
# Bumper Plugin은 ContactsState msg를 사용해야 함.(2 page참고)
# Subscriber
self.sub_collision = rospy.Subscriber('{ROS_Topic_name}',ContactsState, self.collision_callback)
# Callback function example
def collision_callback(self, message):
if message:
print(message.states[0].collision1_name)
print(message.states[0].collision2_name)
print(message.header)
print(message.states)
<gazebo_msgs/ContactsState Message>
http://docs.ros.org/jade/api/gazebo_msgs/html/msg/ContactsState.html

## Slide 6
Topic check(terminal)
$ rostopic list # {ROS_Topic_name}을 확인할 수 있습니다.
$ rostopic echo {ROS_Topic_name} # Collision msg를 확인할 수 있습니다.
# example
rostopic echo turtlebot3/gazebo_contact
Collision이 발생하지 않았다면, States 내용이 [ ]로 출력됩니다.(Not collision, empty msg callback)

## Slide 7
CMakeLists.txt(python Directory)
gazebo_msgs를 python script에서 사용하기 위함.
# CMakeLists.txt 파일에 아래 두 부분에 gazebo_msgs 추가
find_package(catkin REQUIRED COMPONENTS rospy gazebo_msgs)
catkin_package(CATKIN_DEPENDS rospy gazebo_msgs)

## Slide 8
package.xml(python Directory)
gazebo_msgs를 python script에서 사용하기 위함.
# package.xml 파일에 아래 두 줄 추가
<build_depend>gazebo_msgs</build_depend>
<exec_depend>gazebo_msgs</exec_depend>
여기까지 완료가 되면 catkin_make해서 빌드해준다.

## Slide 9
참고자료
https://github.com/ros-simulation/gazebo_ros_pkgs
http://docs.ros.org/jade/api/gazebo_msgs/html/msg/ContactsState.html
http://gazebosim.org/tutorials/?tut=ros_comm
http://gazebosim.org/tutorials?tut=contact_sensor
https://answers.ros.org/question/240076/gazebo-ros-collision-detection/
https://bitbucket.org/theconstructcore/contact_tests/src/master/contact_robots_description/
https://www.youtube.com/watch?v=KidqFt1mymE&feature=emb_logo&ab_channel=TheConstruct
https://answers.gazebosim.org//question/20432/ros-gazebo-detecting-collision-with-a-static-object-using-contact-sensor/
https://github.com/robotology/icub-gazebo/issues/21
https://answers.gazebosim.org//question/5355/adding-ros-integrated-contact-sensors/
https://github.com/erlerobot/gym-gazebo/blob/master/gym_gazebo/envs/MARA/gazebo_mara_top_orient_collision_v0.py
https://github.com/AcutronicRobotics/gym-gazebo2/blob/dashing/gym_gazebo2/envs/MARA/mara_collision_orient.py
https://answers.gazebosim.org//question/12687/problems-while-parsing-gazebo-urdf-elements-with-gazebo7-and-ros-jade/

## Slide 10
사용환경
Ubuntu 18.04 LTS
ROS Melodic
Gazebo 9